## Slide 1
TELEPHONY MANAGER
Online Sanity Testing Platform
A modern web-based tool for remote telephony sanity testing — replacing heavyweight Remote PC sessions with a lightweight, multi-user, real-time browser experience.
LG Electronics | Connected Service Unit
February 2026 | v1.0

## Slide 2
THE PROBLEM — Remote PC Limitations
❌ Remote PC (Current Method)
● Only ONE user can connect at a time (exclusive session)
● Requires full desktop streaming — high bandwidth needed
● Slow & laggy UI — screen refresh delays up to 2-3 seconds
● If connection drops, session is lost entirely
● No parallel testing — team waits for one person to finish
● Device physical access required to troubleshoot
● No automated regression — everything is manual
● DLT logs require separate setup on each PC
● No real-time device status dashboard
● No test history / export capability
● IP conflicts when multiple users try to access
✅ Telephony Manager (Our Solution)
● Multi-user access — unlimited tabs, zero conflicts
● Lightweight browser UI — no screen streaming needed
● Instant command execution — sub-second response
● Session persists even if browser tab is refreshed
● Parallel testing — team works simultaneously
● Remote device access via ADB over network
● Built-in automated regression with CSV export
● DLT bridge auto-configures per user session
● Live device dashboard (IMEI, SIM, Radio, Region)
● Full test history with PASS/FAIL export
● Per-user isolation — no IP or port conflicts

## Slide 3
KEY FEATURES
🖥️
Live Device Dashboard
Real-time status bar showing IMEI, SIM State, Service State, Radio State, Region, SW Version
⚡
One-Click Commands
Execute 50+ telephony commands with pass/fail validation using pattern matching
🔄
Automated Regression
Configure test sequences, set iterations, pause/ resume, and export CSV reports
📡
DLT Bridge
Auto-configures TCP proxy per user for DLT log forwarding — no manual setup needed
👥
Multi-User Support
Each user gets unique client ID, isolated config, separate DLT ports — zero conflicts
🔔
Global Notifications
Real-time popups for ADB changes, IMEI writes, and system events across all users
📊
Multi-Model Support
Toyota, JLR, BMW WAVE LOW/HIGH with auto- detection based on device software version
🛡️
Admin Panel
Add/remove models, commands, categories dynamically without code changes

## Slide 4
TECHNOLOGY STACK
FRONTEND
HTML5 + CSS3 + JavaScript
Modern responsive UI with dark theme
Vanilla JS (No frameworks)
Zero dependencies, fast load, easy maintenance
CSS Variables & Glassmorphism
Premium dark-mode design system
Fetch API + Async/Await
Non-blocking server communication
BACKEND
Node.js + Express.js
Lightweight, event-driven server
ADB (Android Debug Bridge)
Device communication via USB/TCP
net (TCP Module)
DLT proxy bridge for log forwarding
child_process (execAsync)
Shell command execution with timeout
TOOLING & DEPLOYMENT
pkg (by Vercel)
Compiles to standalone .exe — no Node.js needed
Single Binary Distribution
TelephonyManager.exe — just double-click to run
sessionStorage + localStorage
Client-side state persistence per tab
JSON-based Config
Dynamic model/command management via JSON files

## Slide 5
ARCHITECTURE — How the Server Connects
BROWSER CLIENTS
🌐 User A (Tab 1)
clientId: client_a_1xxx
🌐 User B (Tab 2)
clientId: client_b_2xxx
🌐 User C (Tab 3)
clientId: client_c_3xxx
──►
──►
──►
EXPRESS.JS SERVER (Port 3000)
⚙️ Request Router
Maps X-Client-ID header to per-user config (userConfigs Map: clientId → {serial, adb, model})
📋 Command Engine
Executes ADB commands via child_process with timeout, caching & pattern validation
💾 Device Cache
10s TTL cache with Promise.allSettled Stale-cache fallback prevents UI flickering
🔔 Notification Bus
Global notification array polled by all clients ADB changes, IMEI writes broadcast to everyone
──►
──►
TARGET DEVICES
📱 Device A (Toyota)
adb1 -s SERIAL_A
USB / TCP-IP Connected
📱 Device B (BMW)
adb1 -s SERIAL_B
USB / TCP-IP Connected
💡 KEY: Per-User Isolation via X-Client-ID Header
Every browser tab generates a unique clientId (stored in sessionStorage). All API calls include this ID as an HTTP header.
The server maintains a Map<clientId, {serial, adbBinary, model}> so each user independently targets their own device.

## Slide 6
DLT BRIDGE — How Each User Gets Isolated Logs
DLT VIEWER (User's PC)
PUBLIC PORT (Unique per user)
TCP PROXY (Node.js net)
ADB FORWARD (Internal port)
DEVICE (Target)
🖥️ User A
DLT Viewer Port 3490
client_a_1xxx
►
TCP Proxy 0.0.0.0:3490
►
ADB Forward localhost:4490
►
Device A tcp:3490
🖥️ User B
DLT Viewer Port 3491
client_b_2xxx
►
TCP Proxy 0.0.0.0:3491
►
ADB Forward localhost:4491
►
Device B tcp:3490
🖥️ User C
DLT Viewer Port 3492
client_c_3xxx
►
TCP Proxy 0.0.0.0:3492
►
ADB Forward localhost:4492
►
Device A tcp:3490
🔑 How Isolation Works
• Each user picks a UNIQUE public port (e.g., 3490, 3491, 3492)
• Server creates an independent TCP proxy per port, tracked by clientId
• When a tab closes (beforeunload), the proxy is auto-destroyed using sendBeacon
🧹 Auto Cleanup
Tab closes →
Proxy destroyed +
ADB forward removed

## Slide 7
GLOBAL NOTIFICATION SYSTEM
Real-time cross-user notifications — when one user makes a system change, ALL users are alerted instantly.
⚙️ How It Works
1. EVENT TRIGGER
A user performs an action that affects all users (e.g., switches ADB binary, writes IMEI, etc.)
2. SERVER STORES
Server calls addGlobalNotification(type, user, message) Stored in globalNotifications array (last 10 kept)
3. CLIENT POLLS
Every 5s, checkDeviceStatus() fetches /api/device-status Response includes notifications[] array
4. NEW? → POPUP!
Client checks seenNotifIds (localStorage) If new → shows animated system popup with icon
🔔 Notification Types
⚙️ ADB Binary Change
When any user switches between adb1 / adb2 / custom binary → All clients auto-sync their binary
🆔 IMEI Write Event
When IMEI is written to device → All users see updated IMEI immediately on their dashboard
📢 System Announcements
Server-push messages for maintenance, updates, or critical device state changes

## Slide 8
MULTI-MODEL SUPPORT & AUTO-DETECTION
🚗 Toyota (Single SIM)
Standard sldd path 50+ commands Region support: IN, AE, SA, JP
🚗 Toyota (Dual SIM)
Dual SIM commands SIM slot selection Extended telephony
🚗 JLR (Single SIM)
JLR-specific commands Single SIM variant Custom validation
🚗 JLR (Dual SIM)
Dual SIM support JLR platform Full command set
🚗 BMW (WAVE LOW)
Path: /usr/bin/factory/sldd getradiostate (numeric) setradiopower 0/1
🚗 BMW (WAVE HIGH)
Dual SIM BMW /usr/bin/factory/sldd Auto-detected via SW ver
🤖 AUTO-DETECTION: Server reads 'cat etc/version' → If output contains 'WAVE' → auto-switches to BMW model
Also uses sticky version cache: if version read fails temporarily, the model doesn't flip back. Smooth experience.

## Slide 9
AUTOMATED REGRESSION ENGINE
🔄 Regression Features
● Configure test sequences — drag & drop command ordering
● Set iteration count (1 to 1000+ cycles)
● Per-step configurable delay (e.g., 5s between commands)
● Custom parameters for Dial / SMS steps
● Pause / Resume mid-regression without losing progress
● Stop at any time — results preserved
● Live progress bar with current iteration / total
● Real-time PASS / FAIL count on screen
● Module-based quick selection (add all SIM, Network, Call commands)
● Detailed timestamped log for every step
📊 CSV Export Report
One-click export generates a CSV with:
• Iteration # | Step # | Timestamp
• Command Name | Command ID
• Full Output | PASS / FAIL Status
File: regression_report_{model}_{timestamp}.csv
✅ Smart PASS/FAIL Validation
Commands are auto-validated using regex patterns:
• SIM State → expects numeric state value
• Network Type → accepts ANY numeric type (not hardcoded)
• EID → passes even if empty (eUICC optional)
• Radio State → supports both Toyota & BMW formats
• Custom patterns per command ID

## Slide 10
DEPLOYMENT & SUMMARY
🚀 How to Deploy
● 1. Copy TelephonyManager.exe to setup PC
● 2. Connect device via USB (or ADB over TCP/IP)
● 3. Double-click TelephonyManager.exe to start
● 4. Open browser: http://localhost:3000
● 5. Share IP with team: http://<PC-IP>:3000
● 6. Each user opens their own tab — done! ✅
📈 Impact vs Remote PC
Setup Time
30+ min → 10 seconds
Concurrent Users
1 (single session) → Unlimited
Bandwidth Required
High (screen streaming) → Minimal (JSON API)
Regression Testing
Fully manual → Fully automated
DLT Setup
Manual per-PC config → Auto per-user
THANK YOU
Questions & Live Demo
Developed by:
Nitish Kumar
Connected Service Unit | LG Electronics
📧 nitish10.kumar@lge.com
🌐 http://si-nitishk:3000